## Slide 1
Introduction to
Microcontroller
www.pantechsolutions.net

## Slide 2: What is Microcontroller?
In simple term – Microcontroller is a small computer that is capable of performing specific task(s)
  e.g car alarm, washing machine, handphone, PDA…
There are many similar names
  Microprocessor-based system, controller, MCU, MPU, CPU…
They can be grouped into two classification
 MCU - Micro Controller Unit
 MPU - Micro Processor Unit
In general, these microcontroller are the brain of the embedded system

## Slide 3: MCU and MPU
3
Classification | MCU |  |  |  |  | MPU
Chip | Embedded A CPU core, memory, peripherals, IO … into a single chip. |  |  |  |  | Contain only the main processor (CPU core)
Block Diagram of a system | MCU |  |  |  |  | Memory IO MPU Peripheral
 |  | CPU Core | Memory | Peripheral |  | 
 |  |  | IO |  |  | 
General Application Area | Self contained to complete a task. Targeted for small, compact, and low cost system |  |  |  |  | -Need external memory, peripheral to accomplish a task - Targeted for complex, high performance and expandable system
Processor (CPU) Core | 4, 8, 16 bit |  |  |  |  | 32 bit or above
Examples | 8051,pic16f887a,M16, H8, SH1/2 |  |  |  |  | SH3/4,8085
Application | Washing machine, car side mirror, air con |  |  |  |  | Handphone, PDA

## Slide 4: Components within MCU
Processor core
Clock
Low power mode
Memory(ROM/RAM)
Input/Output Port
Timer / Counter/ WDT
PWM
ADC/DAC
Serial Interface
On chip Debug
Bus Controller
Other
Clock -sub | Processor Core | 
Clock -main | RAM | 
ROM
Timer
WDT
LCD
Serial Interface
PWM
PWM
 | Timer
 | Timer
Port | Timer Timer ADC
Example of H8/38024

## Slide 5: i. Processor core
Function
  Fetch and execute machine code from memory
  Efficiency & Effectiveness are determine by its architecture
Architecture Type
  Word Size: 4, 8, 16, 32 Bit
  Contains ALU (Arithmetic Logic Unit) for decision process
  Contains General Registers for temporary storage and data manipulation
  Contains Special Registers (PC, Condition, Stack) to assist in program control
  Instruction Sets
  RISC /CISC
  Running Frequency / Voltage
Possible Measurement
  MIPS (Million Instruction Per Instruction)
    Number of machine instructions that a computer can execute in one second
    Provide only a rough indication for comparison

## Slide 6: ii. Clock
MCU needs a clock input to operate
It can have two clock sources
  A. Main processor clock input
    This clock may be divided or multiply to allow the processor to run at a slower speed (lower power consumption) or higher speed
  B. Sub clock input
    32.768KHz is the usual clock used as this allow accurate generation of a second via a 16 bit counter.
These clocks are normally fed via a crystal and two capacitors to the MCU.
OSC1
OSC2

## Slide 7: iii. Low power mode
Low Power is achieved via various mean
  Running at slower speed, such as sub clock(32.768KHz)
    Sleep mode, sub-active, standby…
  Shutting off unused peripherals
    Module stop mode…
Standby mode consume only 1uA

## Slide 8: iv. Memory (ROM/RAM)
ROM (Read Only Memory)
  For program and fixed data storage
  Size: as low as 1 KByte to as high as 512 KByte
  Example
    Masked ROM
    Flash
    PROM - Programmable Read-Only Memory
      OTP - One-Time Programmable
RAM (Random Access Memory)
  For data storage
  Size: as low as 256 Byte to as high as 4 KByte
  Example
    SRAM

## Slide 9: v. Input / Output Port
Basic interface to control (output) and monitor (Input) external events.
  High current port
    (20mA), so as to drive LED directly.
  Open-collector/drain port
    Interface to higher supply circuitry
    Wired-Nor condition

## Slide 10: vi. Timer / Counter / WDT
Timer (8 or 16 bit) are used to generate or measure timing for events.
  External event trigger the count
  Compare match to perform a task
  …
WDT (WatchDog Timer)
  Every time before the counter reach the predefined value, the working MCU will clear the counter.
  Thus, if the counter is not clear within the specified timing, the WDT will reset the whole MCU as this signify that the MCU has run wild.

## Slide 11: vii. PWM
PWM (Pulse Width Modulation)
– Generate continue pulse of preset duty cycle
This can be used to drive motor.

## Slide 12: viii. ADC/DAC
ADC (Analog-to-Digital Conversion)
  The basic peripheral to interface to the real analog world.
  Characteristic
    Accuracy is determine by number of bits (10,12,14…)
    Sampling frequency
    C
– AVCC
onversion technology ( Resistive ladder, Sigma delta…)
, AVSS and each analog input pins
DAC (Digital-to-Analog Conversion)
– This operate in another way. It output the signal in analog form to the outside world
Transducer
ADC
CPU
Analog
Digital
Real World Data -> Temperature Pressure Sound…

## Slide 13: ix. Serial Interface
There are different serial interfaces
  Asynchronous mode (2400 BaudRate…)
  Synchronous mode (at higher transfer rate)
  USB, I2C, SPI, CAN…(different communication standard)
Use for:
  Communication with other devices, such as external RF module, PC…
Generally used only 3 pins
  Serial In, Serial Out, and Clock

## Slide 14: x. On Chip Debug
Circuitry Incorporated for development and debugging purposes
Usually few pins are required for the PC to control the MCU, via a “JTAG-like” emulator
– Mode pin
Data In/Out
Clock pin
Target Board
USB I/F
PC

## Slide 15: xi. Bus Controller
In the higher performance MCU, a bus controller is incorporated to manage internal and external memory bus.
The external bus may be split into different areas, so that each area can be assigned with different setting
  Refresh controller for DRAM
  Longer wait cycles for slower devices

## Slide 16: xii. Other
There are many possible peripherals that can be integrated into each MCU, to perform specific tasks, such as:
  LCD controller
  PLC
  Ethernet MAC
Other components are:
  Interrupts
  LVD (Low Voltage Detection)
  POR (Power On Reset)

## Slide 17: MCU Connection
MCU
VCC
GND
Clock Mode Reset
Flashing
/Debugging
(Optional)
Supply via battery or wall plug
Output Control Motor, LED,
Input Monitor Temperature, Switches…

## Slide 18: Choosing MCU
Reliability - good
Performance – speed, number of bits, architectures
Power consumption - low
Peripherals – require
Number of I/O pins - enough
ROM/RAM size – enough
Package and Size – manufacturing ease
Development Tool – available and ease of Use
Roadmap – for next expansion
Cost - low
Availability – short lead time
Support – technical team, application notes…

## Slide 19: For more Tutorials
5/24/2011 9:38:29
PM
© Pantech Solutions Pvt Ltd. | All rights reserved
www.pantechsolutions.net
www.pantechsolutions.net
http://www.slideshare.net/pantechsolutions
http://www.scribd.com/pantechsolutions
http://www.youtube.com/pantechsolutions