## Slide 1
Emulating CoAP with Network Namespaces and NeST
Credits: Leslie Monis and Gautam Ramakrishnan, NITK Surathkal

## Slide 2
Agenda
Installation of libcoap library in Ubuntu 20.04
Basic example with CoAP Client and Server
Create network namespaces
Create virtual ethernet (veth) pair to connect network namespaces
Attach ‘veth’ endpoints to network namespaces
Assign IP addresses to ‘veth’ interfaces
Ping from one network namespace to another
Run an iperf test between two network namespaces
Configure an asymmetric link using the traffic control (tc) subsystem of Linux
Example with CoAP Client and Server
<number>

## Slide 3
Installation of libcoap library in Ubuntu 20.04
Install the following packages:
$ sudo apt install git build-essential net-tools asciidoc docbook doxygen libssl-dev gnutls-bin openssl autoconf automake pkg-config libtool
Download libcoap via git
Install libcoap (run the following commands one-by-one)
$ git clone https://github.com/obgm/libcoap
<number>
$ cd libcoap, ./autogen.sh, ./configure, make, sudo make install

## Slide 4
Basic example with CoAP Client and Server
Open a terminal, go to libcoap/examples/ directory and run the Server
Open a new terminal, go to libcoap/examples/ directory and run the Client
Expected Output
$ ./coap-client -m get coap://[::1]/.well-known/core
<number>
$ </>;title="General Info";ct=0,</time>;if="clock";rt="ticks";title="Internal Clock";ct=0;obs,</async>;ct=0,</example_data>;title="Example Data";ct=0;obs
$ ./coap-server

## Slide 5
Topology setup with network namespaces: Create two nodes connected via a direct link
<number>

## Slide 6
# ip netns add client
<number>

## Slide 7
Client
# ip netns add client
#
<number>

## Slide 8
Client
# ip netns add client
# ip netns add server
<number>

## Slide 9
Client
Server
# ip netns add client
# ip netns add server
#
<number>

## Slide 10
Client
Server
# ip netns add client
# ip netns add server
# ip link add eth0 type veth peer name eth1
<number>

## Slide 11
Client
Server
eth0
eth1
# ip netns add client
# ip netns add server
# ip link add eth0 type veth peer name eth1
#
<number>

## Slide 12
Client
Server
eth0
eth1
# ip netns add client
# ip netns add server
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
<number>

## Slide 13
Client
Server
eth0
eth1
# ip netns add client
# ip netns add server
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
#
<number>

## Slide 14
Client
Server
eth0
eth1
# ip netns add client
# ip netns add server
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
<number>

## Slide 15
Client
Server
eth0
eth1
# ip netns add client
# ip netns add server
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
#
<number>

## Slide 16
Client
Server
eth0
eth1
# ip netns add client
# ip netns add server
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
<number>

## Slide 17
Client
Server
eth0
eth1
# ip netns add client
# ip netns add server
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
#
<number>

## Slide 18
Client
Server
eth0
eth1
# ip netns add client
# ip netns add server
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
# ip netns exec server ip link set lo up
<number>

## Slide 19
Client
Server
eth0
eth1
# ip netns add client
# ip netns add server
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
# ip netns exec server ip link set lo up
#
<number>

## Slide 20
Client
Server
eth0
eth1
# ip netns add client
# ip netns add server
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
# ip netns exec server ip link set lo up
# ip netns exec client ip link set eth0 up
<number>

## Slide 21
Client
Server
eth0
eth1
# ip netns add server
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
# ip netns exec server ip link set lo up
# ip netns exec client ip link set eth0 up
#
<number>

## Slide 22
Client
Server
eth0
eth1
# ip netns add server
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
# ip netns exec server ip link set lo up
# ip netns exec client ip link set eth0 up
# ip netns exec server ip link set eth1 up
<number>

## Slide 23
Client
Server
eth0
eth1
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
# ip netns exec server ip link set lo up
# ip netns exec client ip link set eth0 up
# ip netns exec server ip link set eth1 up
#
<number>

## Slide 24
Client
Server
eth0
eth1
# ip link add eth0 type veth peer name eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
# ip netns exec server ip link set lo up
# ip netns exec client ip link set eth0 up
# ip netns exec server ip link set eth1 up
# ip netns exec client ip address add 10.0.0.1/24 dev eth0
<number>

## Slide 25
Client
Server
eth0
eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
# ip netns exec server ip link set lo up
# ip netns exec client ip link set eth0 up
# ip netns exec server ip link set eth1 up
# ip netns exec client ip address add 10.0.0.1/24 dev eth0
#
10.0.0.1/24
<number>

## Slide 26
Client
Server
eth0
eth1
# ip link set eth0 netns client
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
# ip netns exec server ip link set lo up
# ip netns exec client ip link set eth0 up
# ip netns exec server ip link set eth1 up
# ip netns exec client ip address add 10.0.0.1/24 dev eth0
# ip netns exec server ip address add 10.0.0.2/24 dev eth1
10.0.0.1/24
<number>

## Slide 27
Client
Server
eth0
eth1
# ip link set eth1 netns server
# ip netns exec client ip link set lo up
# ip netns exec server ip link set lo up
# ip netns exec client ip link set eth0 up
# ip netns exec server ip link set eth1 up
# ip netns exec client ip address add 10.0.0.1/24 dev eth0
# ip netns exec server ip address add 10.0.0.2/24 dev eth1
#
10.0.0.1/24
10.0.0.2/24
<number>

## Slide 28
Client
Server
eth0
eth1
#
10.0.0.1/24
10.0.0.2/24
#
<number>

## Slide 29
Client
Server
eth0
eth1
# ip netns exec client bash
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
<number>

## Slide 30
Client
Server
eth0
eth1
# ip netns exec client bash
#
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
#
<number>

## Slide 31
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<number>

## Slide 32
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
#
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
#
<number>

## Slide 33
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
#
<number>

## Slide 34
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
<output>
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
#
<number>

## Slide 35
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
<output>^C
#
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
#
<number>

## Slide 36
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
<output>^C
#
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
# ping 10.0.0.1
<number>

## Slide 37
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
<output>^C
#
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
# ping 10.0.0.1
<output>
<number>

## Slide 38
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
<output>^C
#
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
# ping 10.0.0.1
<output>^C
#
<number>

## Slide 39
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
<output>^C
#
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
# ping 10.0.0.1
<output>^C
# iperf -s
<number>

## Slide 40
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
<output>^C
#
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
# ping 10.0.0.1
<output>^C
# iperf -s
<output>
<number>

## Slide 41
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
<output>^C
# iperf -c 10.0.0.2
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
# ping 10.0.0.1
<output>^C
# iperf -s
<output>
<number>

## Slide 42
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
<output>^C
# iperf -c 10.0.0.2
<output>
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
# ping 10.0.0.1
<output>^C
# iperf -s
<output>
<number>

## Slide 43
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
<output>^C
# iperf -c 10.0.0.2
<output>^C
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
# ping 10.0.0.1
<output>^C
# iperf -s
<output>
<number>

## Slide 44
Client
Server
eth0
eth1
# ip netns exec client bash
# ip address
<output>
# ping 10.0.0.2
<output>^C
# iperf -c 10.0.0.2
<output>^C
# iperf -c 10.0.0.2 -u
10.0.0.1/24
10.0.0.2/24
# ip netns exec server bash
# ip address
<output>
# ping 10.0.0.1
<output>^C
# iperf -s
<output>
<number>

## Slide 45
Client
Server
eth0
eth1
#
10.0.0.1/24
10.0.0.2/24
#
noqueue
noqueue
<number>

## Slide 46
# tc qdisc show dev eth0
# tc qdisc show dev eth1
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
noqueue
noqueue
<number>

## Slide 47
# tc qdisc show dev eth0
<output>
#
# tc qdisc show dev eth1
<output>
#
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
noqueue
noqueue
<number>

## Slide 48
# tc qdisc show dev eth0
<output>
# tc qdisc add dev eth0 root \
netem delay 5ms rate 10mbit
# tc qdisc show dev eth1
<output>
#
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
noqueue
noqueue
<number>

## Slide 49
# tc qdisc show dev eth0
<output>
# tc qdisc add dev eth0 root \
netem delay 5ms rate 10mbit
#
# tc qdisc show dev eth1
<output>
#
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
netem
noqueue
<number>

## Slide 50
# tc qdisc show dev eth0
<output>
# tc qdisc add dev eth0 root \
netem delay 5ms rate 10mbit
#
# tc qdisc show dev eth1
<output>
# tc qdisc add dev eth1 root \
netem delay 10ms rate 50mbit
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
netem
noqueue
<number>

## Slide 51
# tc qdisc show dev eth0
<output>
# tc qdisc add dev eth0 root \
netem delay 5ms rate 10mbit
#
# tc qdisc show dev eth1
<output>
# tc qdisc add dev eth1 root \
netem delay 10ms rate 50mbit
#
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
netem
netem
<number>

## Slide 52
Example with CoAP Client and Server using network namespaces
<number>

## Slide 53
# ./coap-client -m get coap://[10.0.0.2]/.well-known/core
# ./coap-server
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
netem
netem
<number>

## Slide 54
Topology setup with NeST: Create two nodes connected via a direct link
<number>

## Slide 55
What is NeST?
A Python package
Uses network namespaces to simplify network experimentation
Provides intuitive APIs to
  Build a virtual network
  Run experiments on the virtual network
  Collect statistics
  Plot results
Shanthanu S. Rai, Narayan G., Dhanasekhar M., Leslie Monis, and Mohit P. Tahiliani. "NeST: Network Stack Tester." In Proceedings of the Applied Networking Research Workshop, pp. 32-37. 2020.
<number>

## Slide 56
Why NeST?
Simplifies the process to reproduce network experiments
Less physical resources, less error prone and less prerequisites
Multiple instances of the same network topology can co-exist, and different experiments can be run in parallel on every instance
Open source tool released under GPLv2 License
<number>

## Slide 57
Installing NeST
$ sudo apt install python3-pip netperf
$ python3 -m pip install -U pip
$ python3 -m pip install nitk-nest
<number>
Website: https://nitk-nest.github.io/
Repository: https://gitlab.com/nitk-nest/nest
NeST users list: https://groups.google.com/g/nest-users
NeST documentation: https://nitk-nest.github.io/docs/index.html

## Slide 58
from nest.experiment import *
from nest.topology import *
<number>
Note: Do not write these commands in a terminal. Kindly open a file editor (e.g., gedit) and type these commands in it. Remember, you have to save it as a python file (with .py extension)

## Slide 59
from nest.experiment import *
from nest.topology import *
client = Node('client')
<number>

## Slide 60
Client
from nest.experiment import *
from nest.topology import *
client = Node('client')
<number>

## Slide 61
Client
from nest.experiment import *
from nest.topology import *
client = Node('client')
server = Node('server')
<number>

## Slide 62
Client
Server
from nest.experiment import *
from nest.topology import *
client = Node('client')
server = Node('server')
<number>

## Slide 63
Client
Server
from nest.topology import *
client = Node('client')
server = Node('server')
(eth0, eth1) = connect(client, server)
<number>

## Slide 64
Client
Server
eth0
eth1
from nest.topology import *
client = Node('client')
server = Node('server')
(eth0, eth1) = connect(client, server)
<number>

## Slide 65
Client
Server
eth0
eth1
from nest.topology import *
client = Node('client')
server = Node('server')
(eth0, eth1) = connect(client, server)
<number>

## Slide 66
Client
Server
eth0
eth1
from nest.topology import *
client = Node('client')
server = Node('server')
(eth0, eth1) = connect(client, server)
<number>

## Slide 67
Client
Server
eth0
eth1
from nest.topology import *
client = Node('client')
server = Node('server')
(eth0, eth1) = connect(client, server)
<number>

## Slide 68
Client
Server
eth0
eth1
from nest.topology import *
client = Node('client')
server = Node('server')
(eth0, eth1) = connect(client, server)
<number>

## Slide 69
Client
Server
eth0
eth1
from nest.topology import *
client = Node('client')
server = Node('server')
(eth0, eth1) = connect(client, server)
<number>

## Slide 70
Client
Server
eth0
eth1
from nest.topology import *
client = Node('client')
server = Node('server')
(eth0, eth1) = connect(client, server)
<number>

## Slide 71
Client
Server
eth0
eth1
client = Node('client')
server = Node('server')
(eth0, eth1) = connect(client, server)
eth0.set_address('10.0.0.1/24')
<number>

## Slide 72
Client
Server
eth0
eth1
client = Node('client')
server = Node('server')
(eth0, eth1) = connect(client, server)
eth0.set_address('10.0.0.1/24')
10.0.0.1/24
<number>

## Slide 73
Client
Server
eth0
eth1
server = Node('server')
(eth0, eth1) = connect(client, server)
eth0.set_address('10.0.0.1/24')
eth1.set_address('10.0.0.2/24')
10.0.0.1/24
<number>

## Slide 74
Client
Server
eth0
eth1
server = Node('server')
(eth0, eth1) = connect(client, server)
eth0.set_address('10.0.0.1/24')
eth1.set_address('10.0.0.2/24')
10.0.0.1/24
10.0.0.2/24
<number>

## Slide 75
Client
Server
eth0
eth1
(eth0, eth1) = connect(client, server)
eth0.set_address('10.0.0.1/24')
eth1.set_address('10.0.0.2/24')
client.ping(eth1.address) # client.ping('10.0.0.2') also works
10.0.0.1/24
10.0.0.2/24
<number>

## Slide 76
(eth0, eth1) = connect(client, server)
eth0.set_address('10.0.0.1/24')
eth1.set_address('10.0.0.2/24')
client.ping(eth1.address) # client.ping('10.0.0.2') also works
<number>
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
noqueue
noqueue

## Slide 77
eth0.set_address('10.0.0.1/24')
eth1.set_address('10.0.0.2/24')
client.ping(eth1.address) # client.ping('10.0.0.2') also works
eth0.set_attributes('5mbit', '5ms')
<number>
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
noqueue
noqueue

## Slide 78
eth0.set_address('10.0.0.1/24')
eth1.set_address('10.0.0.2/24')
client.ping(eth1.address) # client.ping('10.0.0.2') also works
eth0.set_attributes('5mbit', '5ms')
<number>
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
netem
noqueue

## Slide 79
eth1.set_address('10.0.0.2/24')
client.ping(eth1.address) # client.ping('10.0.0.2') also works
eth0.set_attributes('5mbit', '5ms')
eth1.set_attributes('10mbit', '100ms')
<number>
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
netem
noqueue

## Slide 80
eth1.set_address('10.0.0.2/24')
client.ping(eth1.address) # client.ping('10.0.0.2') also works
eth0.set_attributes('5mbit', '5ms')
eth1.set_attributes('10mbit', '100ms')
<number>
Client
Server
eth0
eth1
10.0.0.1/24
10.0.0.2/24
netem
netem

## Slide 81
Thank you!
<number>