## Slide 1
Wireless Embedded Systems
Aaron Schulman
CSE190 Winter 2020
Lecture 2
MCUs and IO

## Slide 2: Reading for next week
Posted on Website – Please skim.
  “ARM Cortex-M for Beginners”

## Slide 3: Introduction to Microcontrollers

## Slide 4: Introduction to Microcontrollers
A microcontroller (MCU) is a small computer on a single integrated circuit consisting of a relatively simple central processing unit (CPU) combined with peripheral devices such as memories, I/O devices, and timers.
  By some accounts, more than half of all CPUs sold worldwide are microcontrollers

## Slide 5: Die shot of a microcontroller

## Slide 6: Microcontroller VS Microprocessor
A microcontroller is a small computer on a single integrated circuit containing a processor core, memory, and programmable input/output peripherals.
A microprocessor incorporates the functions of a computer’s central processing unit (CPU) on a single integrated circuit.

## Slide 7: Microcontroller VS Microprocessor

## Slide 8: Types of Processors
In general-purpose computing, the variety of instruction set architectures today is limited, with the Intel x86 architecture overwhelmingly dominating all.
There is no such dominance in embedded computing. On the contrary, the variety of processors can be daunting to a system designer.
Things that matter
  Peripherals, Concurrency & Timing, Clock Rates, Memory sizes (SRAM & flash), Package sizes

## Slide 9: Types of Microcontrollers

## Slide 10: How to choose MCU for our project?
What metrics we need to consider?
  Power consumption
  Clock frequency
  IO pins
  Memory
  Internal functions
  Others

## Slide 11: How to choose MCU for our project?
What metrics we need to consider?
  Power consumption
    We cannot afford mA MCU because the power budget of the system is 3.47mA.
  Clock frequency (speed that instructions are executed)
    kHz is too slow…
    100MHz is over kill...
  IO pins
    Lots of peripherals - Image sensor, UART debugger, SD card, DAC, ADC, microphone, LED

## Slide 12: How to choose MCU for our project?
What metrics we need to consider?
  Memory
    We need to have sufficient memory to store:
      Program (Non-volatile): Logic to read from sensors, communicate
      Stack: Function calls are now expensive (no recursion)
      Data: Constants (time periods), Sensor history, Communication state
  Internal functions
    Migrating data from the sensor to the radio (DMA)

## Slide 13: How to choose MCU for our project?
Memory
  Store accelerometer history data
    12bits each for X,Y,Z acceleration
    sampled 2 thousand times a second (2 KHz)
    = 12*3*2,000 bits per second (72kbits or 9 kBytes)
    How many seconds can we hold if we have only 100 kBytes of storage
  What types of memory are available on an MCU?
    Internal memory: RAM, 0.5~128 kBytes
    External memory: Flash, high power consumption, ~5mA for read and ~10mA for erase

## Slide 14: How to choose MCU for our project?
Clock frequency
  kHz is too slow
    Smartphone camera frame rate is 60fps (1 KHz clock would leave only 60 clock cycles per frame)
  100MHz is too fast
    Power consumption is high
  Several MHz would be ideal

## Slide 15: How to choose MCU for our project?
IO pins (interface for external peripherals)
  Interfacing sensors, UART debugger, LEDs, Bluetooth
  We need a large number of IO pins
  We need various types of IO pins
    Analog pins (input/output analog signals e.g., audio)
    Digital pins (input/output digital signals e.g., busses, GPIOs)

## Slide 16: The MCU used in our projects

## Slide 17: Input and Output (I/O)

## Slide 18: I/O Devices (sensors)
Keyboard, mouse, microphone, scanner, video/photo camera, etc.
Large diversity
  Many widely differing device types
  Devices within each type also differs
Speed
  varying, often slow access & transfer compared to CPU
  Some device-types require very fast access & transfer
Access
  Sequential VS random
  read, write, read & write

## Slide 19: What operations does software need to perform on peripherals?
Get and set parameters
Receive and transmit data
Enable and disable functions

## Slide 20: How can we imagine providing an interface to hardware from software?
Specialized CPU instructions (x86 in/out)

## Slide 21: Port I/O
Devices registers mapped onto “ports”; a separate address space
Use special I/O instructions to read/write ports
Protected by making I/O instructions available only in kernel/supervisor mode
Used for example by IBM 360 and successors

## Slide 22: How can we imagine providing an interface to hardware from software?
Specialized CPU instructions (x86 in/out)
Treating devices like they are memory (MMIO)

## Slide 23: Memory Mapped IO
Device registers mapped into regular address space
Use regular move (assignment) instructions to read/ write a device’s hardware “registers”
Use memory protection mechanism to protect device registers

## Slide 24: MMIO is used for embedded systems
Why not Ports I/O?
  special I/O instructions would be instruction set dependent (x86, ARM Thumb, MIPS)
    Bad if there are many different instruction sets out there
  Need special hardware to execute and protect instructions
Memory mapped I/O:
  Can use all existing memory reference instructions for I/O
    Can reuse code for reading and writing (e.g., memcpy)
  Memory protection mechanism allows greater flexibility than protected instructions (protect specific registers)
  Can reuse memory management / protection hardware to interface with hardware (saves space and power)

## Slide 25: Reading and writing with MMIO is not like talking to RAM
MMIO reads and writes hardware device registers
Reads and write to registers can cause peripherals to begin or end an operation
By reading data, it may cause the hardware to do something!!!
  E.g., Clear an interrupt flag, get the next byte on a bus
By writing data, it may cause the hardware to do something with it
  E.g., Send this data over the UART bus

## Slide 26: GPIOs are the general digital I/O device
Each GPIO pin represents one bit in memory: if the pin is on it’s a 1, off it’s a 0
That bit can be an input or an output
GPIOs can be used to control lights (light on or off), but even more
Indicating that an event just happened
  Interrupt the radio to tell it to transmit data
  Interrupt the CPU to tell it a button was pressed
  Read pin status to receive configuration messages
Debugging
  Did this one part of my code actually execute?
  Is the timer firing at the interval that I expect it to fire (connect GPIO to oscilloscope)?
  Why using GPIO?
    GPIO ops are lightweight

## Slide 27: Topology of a GPIO pin

## Slide 28: GPIO Configurations

## Slide 29: A fun extra feature: Drive Strength